## Slide 1
Room-side Troffer ODM
Steve Reich, 4/10/2020

## Slide 2: Scope
Cree lighting is looking for:
  Design Engineering and production tooling for the sheetmetal components of our new troffer lineup
  This Includes
    Backpans
    Endpanels
    Center LED trays
  Not included
    Plastic injection molded endcaps
    Extruded diffusion lenses

## Slide 3: Troffer Overview

## Slide 4: Troffer Features - Front
Removable LED/Driver Tray
All lens and end cap options designed and produced by CREE Lighting
All sheet metal and retention clips designed by turnkey provider.
Removable End Caps
Removable Lens
Removable End Caps
Quick Release, Tool-less Retention Clips
Notes: Clip is just a concept. Require ODM to put more thoughts on suppliers to solve the issue. Does not depend on clip contact (thermal resistance). Make them aware of the thermal issue. Internal: mock-up test/sheet metal. Additional thermal relief onto the driver/EB. LED shall be fine. How often (i.e., 10 times) replacement.
Identify the worst thermal combo for testing. Identify the ODM/turnkey supplier. Provide high level requirement & concept. Have supplier work out the details. Worst case weight on Ebom (30% margin). Get quote or requirement template from OEM/ODM team. Provide mini gauge size for tray/panel/pan per UL standard. Prefer the same gauge in the end panel of the same fixture. Based on existing FLX design. Start off FLX.
Check with Dana. Have supplier. Provide “Weight & Thermal” specs.
Pre-painting vs powder coating. Color matters over the paint method. Mounting LED driver is not specified (hole & screws are fine, no shadows).

## Slide 5: Troffer Features - Front
LED Board
LED/Driver Tray
347V Transformer
Emergency Backup
Generator Transfer
Additional Accessories
LED Linear Driver

## Slide 6: Troffer Features - Back
Standard
Bent
T-Grid Integrated Clip

## Slide 7: Troffer Features – Lens Options
All lens options designed and produced by CREE Lighting
Arch
Round
Square

## Slide 8: Troffer - End Cap Options
Wireless Lutron VIVE or CREE WIM
Standard (Not Wireless)
Arch End Caps

## Slide 9: Troffer - End Cap Options
Wireless Lutron VIVE or CREE WIM
Standard (Not Wireless)
Round End Caps

## Slide 10: Troffer - End Cap Options
Wireless
Lutron VIVE or CREE WIM
Standard (Not Wireless)
Square End Caps

## Slide 11: Parts up for Bid for design by turnkey provider
End Panels 2pcs/fixture
  1x4 Version
  2x2/2x4 Version
Back Pan
  1x4 Version
  2x2 Version
  2x4 Version
Removable Tray Assembly
  2x2 Version
  1x4/2x4 Version
  Associated assembly components

## Slide 12: Design Features – End Panels
Features Required
(Locked Design)
Details to be furnished in design package
Features Required
(Semi-Flexible Design)
Details to be furnished in design package
Features Required
(Flexible Design)
2X ½” Trade Knockout
Locate approx. as shown
Chamfer all sharp edges
Notes: Suspending holes (upper left features), position. Strength based on UL requirement

## Slide 13: Design Features – Pans
1.50” Requirement
Features Required
(Flexible Design)
2X Access Cover Locations
Must accept existing P/N LHD00752X
Features Required (Design Flexible)
Overall Fixture Height = 4.10” MAX
4X ½” Trade Knockout
Locate approx. as shown
Pan angles must be maintained. Angles shall be furnished as part of design package

## Slide 14: Design Features – Removable Tray
Actual Driver, EB and Accessory matrix shall be conveyed with design package (Design Flexible)
Design package shall have LED board mounting locations and physical extents
2X Detachable & Tool-less Safety Tethers
Features Required (Design Flexible)
Removable tray design for integration with retention clips (Design Flexible)

## Slide 15: Design Features – Removable Tray
Quick Release Assembly Requirements
  Must be tool-less
  Safety tethered on back side
  Completely removable from room-side
  Quick disconnects for any wire harnesses
  Safely support the weight of LED Driver, EB and Transformer
  Cannot interfere with existing lens profiles
  Cannot create shadows on lens
Removable Assembly Suggestions
  Hardened steel quick release clips
  Slot+Tab lanced sheet metal between tray and pan
  Slide locking action
  Side hinged action
Quick Release Assembly
Features Required (Design Flexible)

## Slide 16: 2X2
Side
Front
Top
604mm/ 23.8”
603mm/ 23.7”
104mm/4.1”

## Slide 17: 2X2

## Slide 18: 1X4
Side
Front
Top
1,213mm 47.8”
298mm/11.8”
104mm/4.1”

## Slide 19: 1X4

## Slide 20: 2X4
Side
Front
Top
1,213mm 47.8”
603mm/23.7”
104mm/4.1”

## Slide 21: 2X4

## Slide 22: Design package details
Beyond the design details in notes (in red previously)
  PRS details for driver/EB/accessory options
  Any pertinent thermal constraints for the driver enclosure portion

## Slide 23: Electrical Components on the LED/Driver Tray
This slide identifies the critical electrical components that need to be mounted on the driver side of LED/Driver tray. It includes 1) LED driver, 2) EB driver, 3) GTDU, 4) SR bridge. Here is the guidance.
Design mounting options on the LED/driver tray to enable the combos below.
Meet the UL compliance requirement handling the max weight.
Test the worst thermal condition (red arrow).
Last Update: 4/14/2020
EE: Qingcong Hu
Sys Eng: Frank Fang